## Slide 1
TinyALU
Verification
presented by
Ahmed Abdellatif - Ahmed Amr - Ahmed Essam
Aya Hassan - Eman Yasser - Essraa Khlaed - Passant Nabil

## Slide 2
Verification Plan

## Slide 3
Architecture

## Slide 4
Assertions

## Slide 5
Reference Model
A reference model was implemented based on the given specifications:
  When the start signal is asserted, The ALU executes the operation selected by the opcode.
  The input operands must remain stable from the assertion of start until the result is generated.
  The operation completes when the done signal is asserted.
  The ALU supports:
1. Three single-cycle operations: ADD - AND - XOR
2. One multi-cycle operation: MULT

## Slide 6
Scoreboard
single-cycle operations: ADD - AND - XOR
Compute the result of single-cycle operation

## Slide 7
Scoreboard
Three-cycle operation: MULT
Compute the result of multi-cycle operation

## Slide 8
Scoreboard
Comparison Between Expected Output and DUT Output
The scoreboard checks correctness by comparing the DUT output against the expected result calculated by the reference model.

## Slide 9
Sequence item
  We have created sequence item represents the transaction that will be sent to the DUT
  The sequence item generate a randomized inputs under some defined constrains based on our specs as shown:
    The reset signal to be off most of the time
    The Start signal to be asserted most of the time
    The Operands A,B to have its Maximum or Minimum values most of the time to achieve the required corner cases
    The opcode to be away from the unused cases

## Slide 10
Main sequence
  Generate test transactions for the TinyALU.
  Randomize the item.
  Check if reset_n is active,we go for continue and go to new operation.

## Slide 11
Single cycle :
  Single-cycle operations: Any op except 4.
  Save A, B, op, start to ensure the input values are stable during the operation.
  Send the item to the driver again with the same values to ensure deterministic behavior.
Main sequence
Randomization with Constraints,we force the randomized item to match saved values.
Save A, B, op, start

## Slide 12
Main sequence
Multi cycle

## Slide 13
Why Error Injection?
  Normal tests verify correct behavior under valid inputs
  Error injection tests verify:
    Robustness of the design
    Proper error detection and handling
What happens if the protocol is violated?
Does the design fail safely?

## Slide 14
Error Injection Strategy
  Error injection is implemented by extending the normal test components:
    Sequence item
    Sequence
    Driver
    Test
  The base functionality is fully reused
  Additional error behavior is added without modifying the original code
  UVM Factory Override is used to:
    Replace the normal sequence item with an error-aware sequence item
    Replace the normal sequence and driver with error-capable versions

## Slide 15
Error injection testcases
  In our error injection tests we aimed to violate two main feature of the specs which are:
    The opcode and the operands must remain stable along the operation until the signal done is asserted
    opcodes 3'b101-3'b111 will be unused
  So we created three test error testcases:
    op_stable_err: in which we will remain the operands stable but change opcode during the opeation
    operands_stable_err: in which we will remain opcode stable but change the operands during the operation
    invalid_opcode: where we will try to inject the unused opcodes

## Slide 16
Changes in error sequence item
  First we added some signals to the base sequence item
To store the values of the opcode and operands at the begging of operation
To choose which of the testcases will be used

## Slide 17
Changes in error sequence item
  Then we added another error sequence item which extends from the base sequence item and have the following constrains
To have one error testcase active at time
To choose which will be changed and which remain stable based on the testcase
To force opcode to be one of the unused values if it’s the active testcase

## Slide 18
  Driver checks error flags and:
    Drives normal values in the first cycle
    Drives corrupted values (*_new) in the next cycle
How Errors Are Driven
Determine the error type to drive accordingly
Drive different opcode

## Slide 19
  Error test extends the base test
  Overrides the base components with errored one.
Changes in Error Test

## Slide 20
Coverage
  measures of which design features have been exercised by the test
  measures coverage of the design structure (branch, statement, toogle, etc.).
  Code coverage
  Functional coverage
  to ensure that the verification process has exercised the design through all of the interesting values.
  measures how much of the implementation has been exercised.

## Slide 21
Code coverage

## Slide 22
Functional collector

## Slide 23
Assertions

## Slide 24
Bugs in the DUT
  First Bug
  The output doesn’t depend on the start.
  As we can see at “op”=1 the “start”=0 so the result should be the same as previous ,but here the DUT execute the operation.

## Slide 25
Bugs in the DUT
  Second Bug
  The “done” signal doesn’t go back to ‘0’ after the operation.
  As we can see the “done” signal keeps high for multiple periods.
Specs: The done signal stays high for only one clock.
We disabled the “done” to see the other bugs

## Slide 26
Thank You